## Solar Monitor SM2-AD Module Specification

Inputs
2x analog differential	0 – 10 V, 0 – 20 mA
1x analog unipolar	0 – 10 V, 0 – 20 mA, 0 – 100 mV, 0 – 20 mV

Outputs
1x analog	0 – 10 V
2 x relay	48 V, 3 A

Interface
RS485	HBUS (DIN rail, bottom pluggable, no external wires needed)
Max. distance	1200 m

Electrical parameters
Power supply	12 – 24 V DC, max. 50 mA [1] (DIN rail HBUS)

Mechanical parameters
Dimensions	35.6 x 89.7 x 62.2 mm
Mounting	DIN rail, wall
Screw terminals	0.5 mm² – 1.5 mm² cable cores
Protection rating	IP20
Operating temperature	-25 .. +60 °C
LED diodes	Status
[1] Power supply 12 V.

## Mechanical Dimensions